Lab Experiment # 4

Arithmetic and Flag Operations

Calvin Ouellet-Ference
A711643
Mr. Markou
Submitted on the 8th of October 2008
Completed on the 4th of October 2008

1. Objectives

The objectives of this experiment were to familiarize with the basic arithmetic operations and to observe flag activity while performing arithmetic operations.

2. Source Code

Note: The data segment for each steps will be put at the end of each corresponding section as the source code is the same for the first four steps, this will be done as well for section 2.2.

2.1.1 Step 1 Source (C = (A +20h) – B))

;==============================================================
; PROGRAM: LAB4A.ASM
;
; AUTHOR: Calvin O. Ference
;
; DESCRIPTION: This program does basic arithmetic operations.
;==============================================================

        ASSUME	cs:code, ds:data

code SEGMENT
main PROC

init:	mov	ax,data
mov	ds,ax

start:	mov	al,vara	;moves the first variable
add	al,20h	;adds the 20h as a constant to vara
sub	al,varb	;subtracts from al varb
mov	varc,al ;wax off [C=(A+20h)-B]

fini: mov	ax,4c00h
        int	21h

main ENDP
code ENDS

2.1.2 Data Segments for Step 1
1.
data	SEGMENT
mrk1	dw	0ffffh
vara	db	20h
varb	db	40h
varc	db	?
mrk2	dw	0ffffh
data	ENDS
        END

2.
data	SEGMENT
mrk1	dw	0ffffh
vara	db	70h
varb	db	10h
varc	db	?
mrk2	dw	0ffffh
data	ENDS
        END

3.
data	SEGMENT
mrk1	dw	0ffffh
vara	db	60h
varb	db	80h
varc	db	?
mrk2	dw	0ffffh
data	ENDS
        END

4.
data	SEGMENT
mrk1	dw	0ffffh
vara	db	0ECh
varb	db	0
varc	db	?
mrk2	dw	0ffffh
data	ENDS
        END

2.1.2 Step 2 Source (C = (A +2000h) – B))

;==============================================================
; PROGRAM: LAB4E.ASM
;
; AUTHOR: Calvin O. Ference
;
; DESCRIPTION: This program does basic arithmetic operations.
;==============================================================

        ASSUME	cs:code, ds:data

code SEGMENT
main PROC

init:	mov	ax,data
mov	ds,ax

start:	mov	ax,vara	;wax on
add	ax,2000h;adds 2000h to vara
sub	ax,varb	;subtracts varb from vara
mov	ax,varc	;wax off

fini: mov	ax,4c00h
        int	21h

main ENDP
code ENDS

2.2.2 Data Segments for Step 2
1.
data	SEGMENT
mrk1	dw	0ffffh
vara	dw	2000h
varb	dw	4000h
varc	dw	?
mrk2	dw	0ffffh
data	ENDS
        END

2.
data	SEGMENT
mrk1	dw	0ffffh
vara	dw	7000h
varb	dw	1000h
varc	dw	?
mrk2	dw	0ffffh
data	ENDS
        END

3.
data	SEGMENT
mrk1	dw	0ffffh
vara	dw	6000h
varb	dw	8000h
varc	dw	?
mrk2	dw	0ffffh
data	ENDS
        END

4.
data	SEGMENT
mrk1	dw	0ffffh
vara	dw	0FF38h
varb	dw	0
varc	dw	?
mrk2	dw	0ffffh
data	ENDS
        END

3. List File

Note: Like in section 2, the data segments of the list files will be separated from the source and will each be put in a separate sub-section.

3.1.1 List File for Step 1

Microsoft (R) Macro Assembler Version 6.11d	10/01/08 15:21:23
lab4a.asm	Page 1 - 1

;==============================================================
; PROGRAM: LAB4A.ASM
;
; AUTHOR: Calvin O. Ference
;
; DESCRIPTION: This program does basic arithmetic operations.
;==============================================================

       ASSUME	cs:code, ds:data

 0000	code SEGMENT
 0000	main PROC

 0000 B8 ---- R	init:	mov	ax,data
 0003 8E D8	mov	ds,ax

 0005 A0 0002 R	start:	mov	al,vara	;moves the first variable
 0008 04 20	add	al,20h	;adds the 20h as a constant to vara
 000A 2A 06 0003 R	sub	al,varb	;subtracts from al varb
 000E A2 0004 R	mov	varc,al ;wax off [C=(A+20h)-B]

 0011 B8 4C00	fini: mov	ax,4c00h
 0014 CD 21	int	21h

 0016	main ENDP
 0016	code ENDS

Microsoft (R) Macro Assembler Version 6.11d	10/01/08 15:21:23
lab4a.asm	Symbols 2 - 1

Segments and Groups:

        N a m e Size Length Align Combine Class

code . . . . . . . . . . . . . .	16 Bit	0016	Para	Private
data . . . . . . . . . . . . . .	16 Bit	0007	Para	Private

Procedures, parameters and locals:

        N a m e Type Value Attr

main . . . . . . . . . . . . . .	P Near	0000	code	Length= 0016 Public
  init . . . . . . . . . . . . .	L Near	0000	code
  start . . . . . . . . . . . .	L Near	0005	code
  fini . . . . . . . . . . . . .	L Near	0011	code

Symbols:

        N a m e Type Value Attr

mrk1 . . . . . . . . . . . . . .	Word	0000	data
mrk2 . . . . . . . . . . . . . .	Word	0005	data
vara . . . . . . . . . . . . . .	Byte	0002	data
varb . . . . . . . . . . . . . .	Byte	0003	data
varc . . . . . . . . . . . . . .	Byte	0004	data

  0 Warnings
  0 Errors

3.1.2 Data Segments for Step 1 List File
1.
 0000	data	SEGMENT
 0000 FFFF	mrk1	dw	0ffffh
 0002 20	vara	db	20h
 0003 40	varb	db	40h
 0004 00	varc	db	?
 0005 FFFF	mrk2	dw	0ffffh
 0007	data	ENDS
       END
2.
 0000	data	SEGMENT
 0000 FFFF	mrk1	dw	0ffffh
 0002 70	vara	db	70h
 0003 10	varb	db	10h
 0004 00	varc	db	?
 0005 FFFF	mrk2	dw	0ffffh
 0007	data	ENDS
       END

3.
 0000	data	SEGMENT
 0000 FFFF	mrk1	dw	0ffffh
 0002 60	vara	db	60h
 0003 80	varb	db	80h
 0004 00	varc	db	?
 0005 FFFF	mrk2	dw	0ffffh
 0007	data	ENDS
       END

4.
 0000	data	SEGMENT
 0000 FFFF	mrk1	dw	0ffffh
 0002 EC	vara	db	0ECh
 0003 00	varb	db	0
 0004 00	varc	db	?
 0005 FFFF	mrk2	dw	0ffffh
 0007	data	ENDS
       END

3.2.1 List File for Step 2

Microsoft (R) Macro Assembler Version 6.11d	10/01/08 15:51:37
lab4e.asm	Page 1 - 1

;==============================================================
; PROGRAM: LAB4E.ASM
;
; AUTHOR: Calvin O. Ference
;
; DESCRIPTION: This program does basic arithmetic operations.
;==============================================================

       ASSUME	cs:code, ds:data

 0000	code SEGMENT
 0000	main PROC

 0000 B8 ---- R	init:	mov	ax,data
 0003 8E D8	mov	ds,ax

 0005 A1 0002 R	start:	mov	ax,vara	;wax on
 0008 05 2000	add	ax,2000h;adds 2000h to vara
 000B 2B 06 0004 R	sub	ax,varb	;subtracts varb from vara
 000F A1 0006 R	mov	ax,varc	;wax off

 0012 B8 4C00	fini: mov	ax,4c00h
 0015 CD 21	int	21h

 0017	main ENDP
 0017	code ENDS

Microsoft (R) Macro Assembler Version 6.11d	10/01/08 15:51:37
lab4e.asm	Symbols 2 - 1

Segments and Groups:

        N a m e Size Length Align Combine Class

code . . . . . . . . . . . . . .	16 Bit	0017	Para	Private
data . . . . . . . . . . . . . .	16 Bit	000A	Para	Private

Procedures, parameters and locals:

        N a m e Type Value Attr

main . . . . . . . . . . . . . .	P Near	0000	code	Length= 0017 Public
  init . . . . . . . . . . . . .	L Near	0000	code
  start . . . . . . . . . . . .	L Near	0005	code
  fini . . . . . . . . . . . . .	L Near	0012	code

Symbols:

        N a m e Type Value Attr

mrk1 . . . . . . . . . . . . . .	Word	0000	data
mrk2 . . . . . . . . . . . . . .	Word	0008	data
vara . . . . . . . . . . . . . .	Word	0002	data
varb . . . . . . . . . . . . . .	Word	0004	data
varc . . . . . . . . . . . . . .	Word	0006	data

  0 Warnings
  0 Errors

3.2.2 Data Segments for Step 2 List File
1.
 0000	data	SEGMENT
 0000 FFFF	mrk1	dw	0ffffh
 0002 2000	vara	dw	2000h
 0004 4000	varb	dw	4000h
 0006 0000	varc	dw	?
 0008 FFFF	mrk2	dw	0ffffh
 000A	data	ENDS
       END

2.
 0000	data	SEGMENT
 0000 FFFF	mrk1	dw	0ffffh
 0002 7000	vara	dw	7000h
 0004 1000	varb	dw	1000h
 0006 0000	varc	dw	?
 0008 FFFF	mrk2	dw	0ffffh
 000A	data	ENDS
       END

3.
 0000	data	SEGMENT
 0000 FFFF	mrk1	dw	0ffffh
 0002 6000	vara	dw	6000h
 0004 8000	varb	dw	8000h
 0006 0000	varc	dw	?
 0008 FFFF	mrk2	dw	0ffffh
 000A	data	ENDS
       END

4.
 0000	data	SEGMENT
 0000 FFFF	mrk1	dw	0ffffh
 0002 FF38	vara	dw	0FF38h
 0004 0000	varb	dw	0
 0006 0000	varc	dw	?
 0008 FFFF	mrk2	dw	0ffffh
 000A	data	ENDS
       END

4. Results

Note: In this section, the highlighted green values are the flags that have been changed while the highlighted yellow values are the data segments of the program.

4.1.1 Step 1 Part 1

Capture file written by TCAP 3.0, TCAP Copyright(c) 1998 Tim Kannel

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>debug lab4a.exe
-d
0E3B:0000 B8 3D 0E 8E D8 A0 02 00-04 20 2A 06 03 00 A2 04 .=....... *.....
0E3B:0010 00 B8 00 4C CD 21 00 00-00 00 00 00 00 00 00 00 ...L.!..........
0E3B:0020 FF FF 20 40 00 FF FF 20-66 69 6C 65 6E 61 6D 65 .. @... filename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-r
AX=0000 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0000 NV UP EI PL NZ NA PO NC
0E3B:0000 B83D0E MOV AX,0E3D
-t

AX=0E3D BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0003 NV UP EI PL NZ NA PO NC
0E3B:0003 8ED8 MOV DS,AX
-t

AX=0E3D BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0005 NV UP EI PL NZ NA PO NC
0E3B:0005 A00200 MOV AL,[0002] DS:0002=20
-t

AX=0E20 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0008 NV UP EI PL NZ NA PO NC
0E3B:0008 0420 ADD AL,20
-t

AX=0E40 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000A NV UP EI PL NZ NA PO NC
0E3B:000A 2A060300 SUB AL,[0003] DS:0003=40
-t

AX=0E00 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000E NV UP EI PL ZR NA PE NC
0E3B:000E A20400 MOV [0004],AL DS:0004=00
-t

AX=0E00 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0011 NV UP EI PL ZR NA PE NC
0E3B:0011 B8004C MOV AX,4C00
-t

AX=4C00 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0014 NV UP EI PL ZR NA PE NC
0E3B:0014 CD21 INT 21
-d
0E3B:0080 2E 0D 0A 57 44 69 73 70-6C 61 79 73 2C 20 73 65 ...WDisplays, se
0E3B:0090 74 73 2C 20 6F 72 20 72-65 6D 6F 76 65 73 20 4D ts, or removes M
0E3B:00A0 53 2D 44 4F 53 20 65 6E-76 69 72 6F 6E 6D 65 6E S-DOS environmen
0E3B:00B0 74 20 76 61 72 69 61 62-6C 65 73 2E 0D 0A 0D 0A t variables.....
0E3B:00C0 53 45 54 20 5B 76 61 72-69 61 62 6C 65 3D 5B 73 SET [variable=[s
0E3B:00D0 74 72 69 6E 67 5D 5D 0D-0A 0D 0A 81 20 20 76 61 tring]]..... va
0E3B:00E0 72 69 61 62 6C 65 20 20-53 70 65 63 69 66 69 65 riable Specifie
0E3B:00F0 73 20 74 68 65 20 65 6E-76 69 72 6F 6E 6D 65 6E s the environmen
-d cs:0
0E3B:0000 B8 3D 0E 8E D8 A0 02 00-04 20 2A 06 03 00 A2 04 .=....... *.....
0E3B:0010 00 B8 00 4C CD 21 00 00-00 00 00 00 00 00 00 00 ...L.!..........
0E3B:0020 FF FF 20 40 00 FF FF 20-66 69 6C 65 6E 61 6D 65 .. @... filename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-q

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>tcap/u

Conclusion from Tracing

When the subtraction operation was performed, the results equaled zero, thus the zero flag (NZ & ZR) was set, this will most likely be used in further operations which requires “IF” type commands.

4.1.2 Step 1 Part 2

Capture file written by TCAP 3.0, TCAP Copyright(c) 1998 Tim Kannel

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>debug lab4b.exe
-d
0E3B:0000 B8 3D 0E 8E D8 A0 02 00-04 20 2A 06 03 00 A2 04 .=....... *.....
0E3B:0010 00 B8 00 4C CD 21 00 00-00 00 00 00 00 00 00 00 ...L.!..........
0E3B:0020 FF FF 70 10 00 FF FF 20-66 69 6C 65 6E 61 6D 65 ..p.... filename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-r
AX=0000 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0000 NV UP EI PL NZ NA PO NC
0E3B:0000 B83D0E MOV AX,0E3D
-t

AX=0E3D BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0003 NV UP EI PL NZ NA PO NC
0E3B:0003 8ED8 MOV DS,AX
-t

AX=0E3D BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0005 NV UP EI PL NZ NA PO NC
0E3B:0005 A00200 MOV AL,[0002] DS:0002=70
-t

AX=0E70 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0008 NV UP EI PL NZ NA PO NC
0E3B:0008 0420 ADD AL,20
-t

AX=0E90 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000A OV UP EI NG NZ NA PE NC
0E3B:000A 2A060300 SUB AL,[0003] DS:0003=10
-t

AX=0E80 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000E NV UP EI NG NZ NA PO NC
0E3B:000E A20400 MOV [0004],AL DS:0004=00
-t

AX=0E80 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0011 NV UP EI NG NZ NA PO NC
0E3B:0011 B8004C MOV AX,4C00
-t

AX=4C00 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0014 NV UP EI NG NZ NA PO NC
0E3B:0014 CD21 INT 21
-d
0E3B:0080 2E 0D 0A 57 44 69 73 70-6C 61 79 73 2C 20 73 65 ...WDisplays, se
0E3B:0090 74 73 2C 20 6F 72 20 72-65 6D 6F 76 65 73 20 4D ts, or removes M
0E3B:00A0 53 2D 44 4F 53 20 65 6E-76 69 72 6F 6E 6D 65 6E S-DOS environmen
0E3B:00B0 74 20 76 61 72 69 61 62-6C 65 73 2E 0D 0A 0D 0A t variables.....
0E3B:00C0 53 45 54 20 5B 76 61 72-69 61 62 6C 65 3D 5B 73 SET [variable=[s
0E3B:00D0 74 72 69 6E 67 5D 5D 0D-0A 0D 0A 81 20 20 76 61 tring]]..... va
0E3B:00E0 72 69 61 62 6C 65 20 20-53 70 65 63 69 66 69 65 riable Specifie
0E3B:00F0 73 20 74 68 65 20 65 6E-76 69 72 6F 6E 6D 65 6E s the environmen
-d cs:0
0E3B:0000 B8 3D 0E 8E D8 A0 02 00-04 20 2A 06 03 00 A2 04 .=....... *.....
0E3B:0010 00 B8 00 4C CD 21 00 00-00 00 00 00 00 00 00 00 ...L.!..........
0E3B:0020 FF FF 70 10 80 FF FF 20-66 69 6C 65 6E 61 6D 65 ..p.... filename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-q

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>tcap/u

Conclusion from Tracing

Two flags were changed during this operation, the overflow flag (NV & OV) and the parity flag (PO & PE). The overflow flag was triggered when adding 20h to 70h, which passed the “middle” border between positive and negative values which are of 7Fh and 80h, afterwards when removing 10h from 90h, the overflow flag went back to 0 because the result did not went lower then 80h so no overflow occurred. The parity flag was set to 1 when the addition of 20h occurred then reverted back to 0 when the subtraction was performed. The understanding of what the parity flags does is when in a byte, the amount of 1-bits in the value is an even number. In this case we had the following binary bytes:

70h	0111 0000b	(odd)
90h	1001 0000b	(even)
80h	1000 0000b	(odd)

the parity flag was set to 1 right after the addition, then back to 0 after the subtraction, thus this should make sense but further studying will be performed to fully grasp the concept of this flag and if this is correct.

4.1.3 Step 1 Part 3

Capture file written by TCAP 3.0, TCAP Copyright(c) 1998 Tim Kannel

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>debug lab4c.exe
-d
0E3B:0000 B8 3D 0E 8E D8 A0 02 00-04 20 2A 06 03 00 A2 04 .=....... *.....
0E3B:0010 00 B8 00 4C CD 21 00 00-00 00 00 00 00 00 00 00 ...L.!..........
0E3B:0020 FF FF 60 80 00 FF FF 20-66 69 6C 65 6E 61 6D 65 ..`.... filename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-r
AX=0000 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0000 NV UP EI PL NZ NA PO NC
0E3B:0000 B83D0E MOV AX,0E3D
-t

AX=0E3D BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0003 NV UP EI PL NZ NA PO NC
0E3B:0003 8ED8 MOV DS,AX
-t

AX=0E3D BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0005 NV UP EI PL NZ NA PO NC
0E3B:0005 A00200 MOV AL,[0002] DS:0002=60
-t

AX=0E60 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0008 NV UP EI PL NZ NA PO NC
0E3B:0008 0420 ADD AL,20
-t

AX=0E80 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000A OV UP EI NG NZ NA PO NC
0E3B:000A 2A060300 SUB AL,[0003] DS:0003=80
-t

AX=0E00 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000E NV UP EI PL ZR NA PE NC
0E3B:000E A20400 MOV [0004],AL DS:0004=00
-t

AX=0E00 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0011 NV UP EI PL ZR NA PE NC
0E3B:0011 B8004C MOV AX,4C00
-t

AX=4C00 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0014 NV UP EI PL ZR NA PE NC
0E3B:0014 CD21 INT 21
-d
0E3B:0080 2E 0D 0A 57 44 69 73 70-6C 61 79 73 2C 20 73 65 ...WDisplays, se
0E3B:0090 74 73 2C 20 6F 72 20 72-65 6D 6F 76 65 73 20 4D ts, or removes M
0E3B:00A0 53 2D 44 4F 53 20 65 6E-76 69 72 6F 6E 6D 65 6E S-DOS environmen
0E3B:00B0 74 20 76 61 72 69 61 62-6C 65 73 2E 0D 0A 0D 0A t variables.....
0E3B:00C0 53 45 54 20 5B 76 61 72-69 61 62 6C 65 3D 5B 73 SET [variable=[s
0E3B:00D0 74 72 69 6E 67 5D 5D 0D-0A 0D 0A 81 20 20 76 61 tring]]..... va
0E3B:00E0 72 69 61 62 6C 65 20 20-53 70 65 63 69 66 69 65 riable Specifie
0E3B:00F0 73 20 74 68 65 20 65 6E-76 69 72 6F 6E 6D 65 6E s the environmen
-d cs:0
0E3B:0000 B8 3D 0E 8E D8 A0 02 00-04 20 2A 06 03 00 A2 04 .=....... *.....
0E3B:0010 00 B8 00 4C CD 21 00 00-00 00 00 00 00 00 00 00 ...L.!..........
0E3B:0020 FF FF 60 80 00 FF FF 20-66 69 6C 65 6E 61 6D 65 ..`.... filename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-q

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>tcap/u

Conclusion from Tracing

Only one new flag was seen in this operation, which is the sign flag (PL & NG). The overflow, zero and parity flags were set during this operation. The overflow flag changed when adding 20h to 60h, which resulted in 80h which is one unit away from the “middle” line between positive and negative values. While the zero flag was set when subtracting 80h to 80h, which resulted in 0. The parity flag was set to 1 when the subtraction occurred, the reason behind this is unknown as the resulting operation is 0. Finally, the sign flag was set to 1 after the addition operation which resulted in 90h which went into the negative section of the number circle, thus the sign flag but when the last operation was performed, the range of the value stayed in the negative range which is what probably caused the sign flag to reset to 0.

4.1.4 Step 1 Part 4

Capture file written by TCAP 3.0, TCAP Copyright(c) 1998 Tim Kannel

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>debug lab4d.exe
-d
0E3B:0000 B8 3D 0E 8E D8 A0 02 00-04 20 2A 06 03 00 A2 04 .=....... *.....
0E3B:0010 00 B8 00 4C CD 21 00 00-00 00 00 00 00 00 00 00 ...L.!..........
0E3B:0020 FF FF EC 00 00 FF FF 01-FF FF 6C 65 6E 61 6D 65 ..........lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-r
AX=0000 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0000 NV UP EI PL NZ NA PO NC
0E3B:0000 B83D0E MOV AX,0E3D
-t

AX=0E3D BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0003 NV UP EI PL NZ NA PO NC
0E3B:0003 8ED8 MOV DS,AX
-t

AX=0E3D BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0005 NV UP EI PL NZ NA PO NC
0E3B:0005 A00200 MOV AL,[0002] DS:0002=EC
-t

AX=0EEC BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0008 NV UP EI PL NZ NA PO NC
0E3B:0008 0420 ADD AL,20
-t

AX=0E0C BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000A NV UP EI PL NZ NA PE CY
0E3B:000A 2A060300 SUB AL,[0003] DS:0003=00
-t

AX=0E0C BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000E NV UP EI PL NZ NA PE NC
0E3B:000E A20400 MOV [0004],AL DS:0004=00
-t

AX=0E0C BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0011 NV UP EI PL NZ NA PE NC
0E3B:0011 B8004C MOV AX,4C00
-t

AX=4C00 BX=0000 CX=0027 DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0014 NV UP EI PL NZ NA PE NC
0E3B:0014 CD21 INT 21
-d
0E3B:0080 2E 0D 0A 57 44 69 73 70-6C 61 79 73 2C 20 73 65 ...WDisplays, se
0E3B:0090 74 73 2C 20 6F 72 20 72-65 6D 6F 76 65 73 20 4D ts, or removes M
0E3B:00A0 53 2D 44 4F 53 20 65 6E-76 69 72 6F 6E 6D 65 6E S-DOS environmen
0E3B:00B0 74 20 76 61 72 69 61 62-6C 65 73 2E 0D 0A 0D 0A t variables.....
0E3B:00C0 53 45 54 20 5B 76 61 72-69 61 62 6C 65 3D 5B 73 SET [variable=[s
0E3B:00D0 74 72 69 6E 67 5D 5D 0D-0A 0D 0A 81 20 20 76 61 tring]]..... va
0E3B:00E0 72 69 61 62 6C 65 20 20-53 70 65 63 69 66 69 65 riable Specifie
0E3B:00F0 73 20 74 68 65 20 65 6E-76 69 72 6F 6E 6D 65 6E s the environmen
-d cs:0
0E3B:0000 B8 3D 0E 8E D8 A0 02 00-04 20 2A 06 03 00 A2 04 .=....... *.....
0E3B:0010 00 B8 00 4C CD 21 00 00-00 00 00 00 00 00 00 00 ...L.!..........
0E3B:0020 FF FF EC 00 0C FF FF 01-FF FF 6C 65 6E 61 6D 65 ..........lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-q

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>tcap/u

Conclusion from Tracing

Two flags were touched during this operation: the parity flag and the carry flag. The result of the addition of ECh and 20h was of 10Ch, which is out of the range of a byte. So the carry flag was set to 1 after this operation, and because nothing was subtracted afterwards, 10Ch remained the same and so did the carry flag. The parity flag was set as well because the value which was stored was simply 0Ch, which is 1100b is an even number, so the parity flag was set because of this.

4.2.1 Step 1 Part 1

Capture file written by TCAP 3.0, TCAP Copyright(c) 1998 Tim Kannel

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>debug lab4e.exe
-d
0E3B:0000 B8 3D 0E 8E D8 A1 02 00-05 00 20 2B 06 04 00 A1 .=........ +....
0E3B:0010 06 00 B8 00 4C CD 21 00-00 00 00 00 00 00 00 00 ....L.!.........
0E3B:0020 FF FF 00 20 00 40 00 00-FF FF 6C 65 6E 61 6D 65 ... .@....lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-r
AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0000 NV UP EI PL NZ NA PO NC
0E3B:0000 B83D0E MOV AX,0E3D
-t

AX=0E3D BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0003 NV UP EI PL NZ NA PO NC
0E3B:0003 8ED8 MOV DS,AX
-t

AX=0E3D BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0005 NV UP EI PL NZ NA PO NC
0E3B:0005 A10200 MOV AX,[0002] DS:0002=2000
-t

AX=2000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0008 NV UP EI PL NZ NA PO NC
0E3B:0008 050020 ADD AX,2000
-t

AX=4000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000B NV UP EI PL NZ NA PE NC
0E3B:000B 2B060400 SUB AX,[0004] DS:0004=4000
-t

AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000F NV UP EI PL ZR NA PE NC
0E3B:000F A10600 MOV AX,[0006] DS:0006=0000
-t

AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0012 NV UP EI PL ZR NA PE NC
0E3B:0012 B8004C MOV AX,4C00
-t

AX=4C00 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0015 NV UP EI PL ZR NA PE NC
0E3B:0015 CD21 INT 21
-r
AX=4C00 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0015 NV UP EI PL ZR NA PE NC
0E3B:0015 CD21 INT 21
-d
0E3B:0080 2E 0D 0A 57 44 69 73 70-6C 61 79 73 2C 20 73 65 ...WDisplays, se
0E3B:0090 74 73 2C 20 6F 72 20 72-65 6D 6F 76 65 73 20 4D ts, or removes M
0E3B:00A0 53 2D 44 4F 53 20 65 6E-76 69 72 6F 6E 6D 65 6E S-DOS environmen
0E3B:00B0 74 20 76 61 72 69 61 62-6C 65 73 2E 0D 0A 0D 0A t variables.....
0E3B:00C0 53 45 54 20 5B 76 61 72-69 61 62 6C 65 3D 5B 73 SET [variable=[s
0E3B:00D0 74 72 69 6E 67 5D 5D 0D-0A 0D 0A 81 20 20 76 61 tring]]..... va
0E3B:00E0 72 69 61 62 6C 65 20 20-53 70 65 63 69 66 69 65 riable Specifie
0E3B:00F0 73 20 74 68 65 20 65 6E-76 69 72 6F 6E 6D 65 6E s the environmen
-d cs:0
0E3B:0000 B8 3D 0E 8E D8 A1 02 00-05 00 20 2B 06 04 00 A1 .=........ +....
0E3B:0010 06 00 B8 00 4C CD 21 00-00 00 00 00 00 00 00 00 ....L.!.........
0E3B:0020 FF FF 00 20 00 40 00 00-FF FF 6C 65 6E 61 6D 65 ... .@....lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-q

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>tcap/u

Conclusion from Tracing

Only the zero flag was set during this operation after the subtraction process of removing 4000h of 4000h.

4.2.2 Step 1 Part 2

Capture file written by TCAP 3.0, TCAP Copyright(c) 1998 Tim Kannel

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>debug lab4f.exe
-d
0E3B:0000 B8 3D 0E 8E D8 A1 02 00-05 00 20 2B 06 04 00 A1 .=........ +....
0E3B:0010 06 00 B8 00 4C CD 21 00-00 00 00 00 00 00 00 00 ....L.!.........
0E3B:0020 FF FF 00 70 00 10 00 00-FF FF 6C 65 6E 61 6D 65 ...p......lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-r
AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0000 NV UP EI PL NZ NA PO NC
0E3B:0000 B83D0E MOV AX,0E3D
-t

AX=0E3D BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0003 NV UP EI PL NZ NA PO NC
0E3B:0003 8ED8 MOV DS,AX
-t

AX=0E3D BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0005 NV UP EI PL NZ NA PO NC
0E3B:0005 A10200 MOV AX,[0002] DS:0002=7000
-t

AX=7000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0008 NV UP EI PL NZ NA PO NC
0E3B:0008 050020 ADD AX,2000
-t

AX=9000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000B OV UP EI NG NZ NA PE NC
0E3B:000B 2B060400 SUB AX,[0004] DS:0004=1000
-t

AX=8000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000F NV UP EI NG NZ NA PE NC
0E3B:000F A10600 MOV AX,[0006] DS:0006=0000
-t

AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0012 NV UP EI NG NZ NA PE NC
0E3B:0012 B8004C MOV AX,4C00
-t

AX=4C00 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0015 NV UP EI NG NZ NA PE NC
0E3B:0015 CD21 INT 21
-d
0E3B:0080 2E 0D 0A 57 44 69 73 70-6C 61 79 73 2C 20 73 65 ...WDisplays, se
0E3B:0090 74 73 2C 20 6F 72 20 72-65 6D 6F 76 65 73 20 4D ts, or removes M
0E3B:00A0 53 2D 44 4F 53 20 65 6E-76 69 72 6F 6E 6D 65 6E S-DOS environmen
0E3B:00B0 74 20 76 61 72 69 61 62-6C 65 73 2E 0D 0A 0D 0A t variables.....
0E3B:00C0 53 45 54 20 5B 76 61 72-69 61 62 6C 65 3D 5B 73 SET [variable=[s
0E3B:00D0 74 72 69 6E 67 5D 5D 0D-0A 0D 0A 81 20 20 76 61 tring]]..... va
0E3B:00E0 72 69 61 62 6C 65 20 20-53 70 65 63 69 66 69 65 riable Specifie
0E3B:00F0 73 20 74 68 65 20 65 6E-76 69 72 6F 6E 6D 65 6E s the environmen
-d cs:0
0E3B:0000 B8 3D 0E 8E D8 A1 02 00-05 00 20 2B 06 04 00 A1 .=........ +....
0E3B:0010 06 00 B8 00 4C CD 21 00-00 00 00 00 00 00 00 00 ....L.!.........
0E3B:0020 FF FF 00 70 00 10 00 00-FF FF 6C 65 6E 61 6D 65 ...p......lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-q

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>tcap/u

Conclusion from Tracing

Three flags were set during this operation. The first one being the overflow flag, which was set right after the addition was performed which resulted in 9000h, which is after the threshold line between positive and negative values (after 7FFF). It was set back to 0 after the subtraction process which resulted in 8000h which did not caused any overflow. The second flag was the sign flag, this was set to 1 when the overflow occurred signaling that it went into the negative range of values and did not revert back after the subtraction process because 8000h is part of the negative value range. Finally the parity flag was set as well after the addition process. 9000H in binary is 1001 0000 0000 0000b which has an even amount of 1-bit values.

4.2.3 Step 1 Part 3

Capture file written by TCAP 3.0, TCAP Copyright(c) 1998 Tim Kannel

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>debug lab4g.exe
-
-d
0E3B:0000 B8 3D 0E 8E D8 A1 02 00-05 00 20 2B 06 04 00 A1 .=........ +....
0E3B:0010 06 00 B8 00 4C CD 21 00-00 00 00 00 00 00 00 00 ....L.!.........
0E3B:0020 FF FF 00 60 00 80 00 00-FF FF 6C 65 6E 61 6D 65 ...`......lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-r
AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0000 NV UP EI PL NZ NA PO NC
0E3B:0000 B83D0E MOV AX,0E3D
-t

AX=0E3D BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0003 NV UP EI PL NZ NA PO NC
0E3B:0003 8ED8 MOV DS,AX
-t

AX=0E3D BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0005 NV UP EI PL NZ NA PO NC
0E3B:0005 A10200 MOV AX,[0002] DS:0002=6000
-t

AX=6000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0008 NV UP EI PL NZ NA PO NC
0E3B:0008 050020 ADD AX,2000
-t

AX=8000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000B OV UP EI NG NZ NA PE NC
0E3B:000B 2B060400 SUB AX,[0004] DS:0004=8000
-t

AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000F NV UP EI PL ZR NA PE NC
0E3B:000F A10600 MOV AX,[0006] DS:0006=0000
-t

AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0012 NV UP EI PL ZR NA PE NC
0E3B:0012 B8004C MOV AX,4C00
-t

AX=4C00 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0015 NV UP EI PL ZR NA PE NC
0E3B:0015 CD21 INT 21
-d
0E3B:0080 2E 0D 0A 57 44 69 73 70-6C 61 79 73 2C 20 73 65 ...WDisplays, se
0E3B:0090 74 73 2C 20 6F 72 20 72-65 6D 6F 76 65 73 20 4D ts, or removes M
0E3B:00A0 53 2D 44 4F 53 20 65 6E-76 69 72 6F 6E 6D 65 6E S-DOS environmen
0E3B:00B0 74 20 76 61 72 69 61 62-6C 65 73 2E 0D 0A 0D 0A t variables.....
0E3B:00C0 53 45 54 20 5B 76 61 72-69 61 62 6C 65 3D 5B 73 SET [variable=[s
0E3B:00D0 74 72 69 6E 67 5D 5D 0D-0A 0D 0A 81 20 20 76 61 tring]]..... va
0E3B:00E0 72 69 61 62 6C 65 20 20-53 70 65 63 69 66 69 65 riable Specifie
0E3B:00F0 73 20 74 68 65 20 65 6E-76 69 72 6F 6E 6D 65 6E s the environmen
-d cs:0
0E3B:0000 B8 3D 0E 8E D8 A1 02 00-05 00 20 2B 06 04 00 A1 .=........ +....
0E3B:0010 06 00 B8 00 4C CD 21 00-00 00 00 00 00 00 00 00 ....L.!.........
0E3B:0020 FF FF 00 60 00 80 00 00-FF FF 6C 65 6E 61 6D 65 ...`......lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-q

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>tcap/u

Conclusion from Tracing

Three flags were changed during this operation. First, the overflow flag was set to 1 when the addition occurred which resulted in 8000h which right after the threshold between the positive and negative values. The overflow flag was set to 0 after the subtraction process of 8000h, which also made the zero flag to go to 1 as the resulting operation was 0 and caused an overflow. Finally the parity flag was set to 1 after the addition but no reason was found, as the binary value for 8000h is 1000 0000 0000 0000b which is clearly as odd 1-bits.

4.2.4 Step 1 Part 4

Capture file written by TCAP 3.0, TCAP Copyright(c) 1998 Tim Kannel

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>debug lab4h.exe
-d
0E3B:0000 B8 3D 0E 8E D8 A1 02 00-05 00 20 2B 06 04 00 A1 .=........ +....
0E3B:0010 06 00 B8 00 4C CD 21 00-00 00 00 00 00 00 00 00 ....L.!.........
0E3B:0020 FF FF 38 FF 00 00 00 00-FF FF 6C 65 6E 61 6D 65 ..8.......lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-r
AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0000 NV UP EI PL NZ NA PO NC
0E3B:0000 B83D0E MOV AX,0E3D
-t

AX=0E3D BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E2B ES=0E2B SS=0E3B CS=0E3B IP=0003 NV UP EI PL NZ NA PO NC
0E3B:0003 8ED8 MOV DS,AX
-t

AX=0E3D BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0005 NV UP EI PL NZ NA PO NC
0E3B:0005 A10200 MOV AX,[0002] DS:0002=FF38
-t

AX=FF38 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0008 NV UP EI PL NZ NA PO NC
0E3B:0008 050020 ADD AX,2000
-t

AX=1F38 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000B NV UP EI PL NZ NA PO CY
0E3B:000B 2B060400 SUB AX,[0004] DS:0004=0000
-t

AX=1F38 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=000F NV UP EI PL NZ NA PO NC
0E3B:000F A10600 MOV AX,[0006] DS:0006=0000
-t

AX=0000 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0012 NV UP EI PL NZ NA PO NC
0E3B:0012 B8004C MOV AX,4C00
-t

AX=4C00 BX=0000 CX=002A DX=0000 SP=0000 BP=0000 SI=0000 DI=0000
DS=0E3D ES=0E2B SS=0E3B CS=0E3B IP=0015 NV UP EI PL NZ NA PO NC
0E3B:0015 CD21 INT 21
-d cs:0
0E3B:0000 B8 3D 0E 8E D8 A1 02 00-05 00 20 2B 06 04 00 A1 .=........ +....
0E3B:0010 06 00 B8 00 4C CD 21 00-00 00 00 00 00 00 00 00 ....L.!.........
0E3B:0020 FF FF 38 FF 00 00 00 00-FF FF 6C 65 6E 61 6D 65 ..8.......lename
0E3B:0030 32 0D 0A 0D 0A 4D 4E 6F-74 65 20 74 68 61 74 20 2....MNote that
0E3B:0040 79 6F 75 20 63 61 6E 6E-6F 74 20 73 70 65 63 69 you cannot speci
0E3B:0050 66 79 20 61 20 6E 65 77-20 64 72 69 76 65 20 6F fy a new drive o
0E3B:0060 72 20 70 61 74 68 20 66-6F 72 20 79 6F 75 72 20 r path for your
0E3B:0070 64 65 73 74 69 6E 61 74-69 6F 6E 20 66 69 6C 65 destination file
-q

G:\USB\ELECTR~1\SEMEST~1\243-31~1\LAB4~1>tcap /u

Conclusion from Tracing

For the final operation, only one flag changed, which was the carry flag. The carry flag went to 1 after the addition process, which resulted in 11F38h which is clearly over the range of a word. Thus the cary flag was set. But after the subtraction process happened (of 0), the flag reverted back to 0 as no carry value higher then FFFFh was present (in this case, 1F38h).

5. Questions

5.1
It is set when the value of either a byte or a word went higher then it can support. i.e. in a byte when it goes higher than FF and in a word when it goes higher than FFFF.

5.2
The overflow is set when after an operation, the values goes in the negative range of the number circly. i.e. in a byte, when it passes from 7Fh to 80h or more and in a word when it passes from 7FFFh to 8000h or more.

5.3
It changes it's condition when an after an operation the result is 0, it will set the zero flag to 1.

5.4
The numeric range is of 0 to 255 or FFh and the carry flag will be set when we go over it's limitations.

5.5
The numeric range is of -126 to 127. The carry flag will be set when going over the limitations, while the overflow flag will be set when passing from 7Fh (127) to 80h (-126).

5.6
No, because if you look at the x86 Instruction set under the MOV command, the Flag section is left out blank, thus no flags will be affected while performing that operation.

5. Conclusion

The experiment was completed successfully and without difficulty. A better understanding of how the flags work and knowing how important and useful they are, thus completing the objective of this experiment.